## Slide 1
VEHICULAR-SPEED-DETECTION
Computer Vision
Presented by
Uday Kiran G-B210506CS
L Mohan Nayak-B210575CS
P Partha Saradhi Reddy-B210582CS
Rahul Naik S-B210477CS

## Slide 2
2 : Background subtraction
TABLE OF CONTENTS
1 : Introduction
5: Comparison
4: YoloV8
3: Haar cascades
7: Output and Results
8 : Conclusion
6 :Custom tracker

## Slide 3
INTRODUCTION
  Objective : To develop a vehicle detection and speed tracking system using both traditional computer vision techniques (Haar Cascades and Background Subtraction) and a modern deep learning approach (YOLOv8).
  Approach Overview: We experimented with three different methods for detecting and calculating the speed of vehicles:
  Methods:
    Background Subtraction
    Haar Cascades
    YOLOv8

## Slide 4
TRADITIONAL METHOD 1 - BACKGROUND SUBTRACTION
Approach: (motion based)
Tools:
  Pure background subtraction using MOG2.
  Contour detection to extract moving blobs.
  Tracked centroid of each blob frame-by-frame.
Speed Estimation:
  Defined two horizontal lines (red and blue).
  Tracked centroids and timestamped when a vehicle crossed each line.
Challenges:
  Poor accuracy with noisy or static background.
  Difficulty distinguishing between object types (bike vs car vs truck).
  Prone to false positives.

## Slide 5
TRADITIONAL METHOD 1 - BACKGROUND SUBTRACTION
Technical Aspects:
  Background subtraction isolates moving objects by comparing frames over time.
  KNN model dynamically updates the background model for better adaptability.
  Contour analysis used to extract bounding boxes.
  Speed = Distance / Time; Time measured via frame timestamps
Output:
  Annotated video with speed overlay
  Speed values saved in CSV format

## Slide 6
TRADITIONAL METHOD 2 - HAAR CASCADE
BACKGROUND SUBTRACTION
Approach:(object based)
Tools:
  Haar Cascade classifier for vehicle detection.
  Centroid tracking to follow vehicles across frames.
  Frame-by-frame analysis to monitor object movement.
Speed Estimation:
  Defined two horizontal lines (red and blue).
  Tracked centroids and timestamped when a vehicle crossed each line.
Challenges:
  Not very robust under occlusion or lighting changes.
  Haar cascade often missed bikes or trucks.
  Dual bounding boxes from Haar and background subtraction needed merging.

## Slide 7
TRADITIONAL METHOD 2 - HAAR CASCADE
BACKGROUND SUBTRACTION
Technical Aspects:
  Haar cascade classifiers work using edge/line features learned via AdaBoost.
  Fast detection using integral image and cascade stages.
  Limited robustness to small objects or varied angles.
  Speed calculated using frame timestamps across defined lines.
Output:
  Video output with detection bounding boxes and speed
  CSV of vehicle speeds

## Slide 8
DEEP LEARNING METHOD -YOLOV8
Tools:
- YOLOv8s model for real-time object detection.
- Custom object tracker for assigning consistent IDs across frames.
- Speed calculated using timestamps as vehicles crossed reference lines.
Speed Estimation:
- Red and blue lines placed 10 meters apart in real-world scale.
- Used time difference between crossings to estimate speed:
Advantages:
- High accuracy in detecting cars, buses, motorcycles, trucks.
- Tracked each vehicle with a unique ID and exported speeds to CSV.

## Slide 9
Comparison Table
Method
  Detection
  Accuracy
  Speed Estimation
  Complexity
Background Subtraction
Motion-based
Low
Frame count
Low
Haar Cascade
Pre-trained classifiers
Medium
Frame-count
Medium
YOLOv8
Deep Learning
High
Time-based
High

## Slide 10
CUSTOM TRACKER FOR VEHICLE TRACKING
Tracker Class:
  Initializes an object with no vehicles detected and an ID counter.
  Tracks the center points of bounding boxes across frames.
  Assigns new IDs to vehicles that are not previously detected.

## Slide 11
Speed Formula:
  Speed is calculated based on the distance moved by the vehicle between frames and the time taken for the movement.
  Distance (in meters) = Pixel distance * Conversion factor.
  Speed (in km/h) = (Distance / Time) * 3.6
SPEED CALCULATION
Code Snippet:

## Slide 12
OUTPUT AND RESULTS
Video Output:
  The processed video with bounding boxes, vehicle IDs, and speed information is saved.
  Speed information is overlayed on the video frame.
Speed CSV:
  Average speeds of each tracked vehicle are saved in a CSV file.

## Slide 13
CONCLUSION
Summary:
  Feature Traditional CV Deep Learning (YOLO)
  Feature Extraction Manual Automatic
  Accuracy Moderate High
  Adaptability Low High
  Real-time Capability High High
  Robust to Variations No Yes

## Slide 14
THANK YOU